Chapter 7 Quiz

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions:	Write the correct answers on the blanks provided.

1.	A means of egress system must terminate in a public way. (264)

A.	True

B.	False

2.	The exit access leads from an occupied portion of a building to the exit. (264)

A.	True

B.	False

3.	Doors must open in the direction of travel away from the primary exit. (269)

A.	True

B.	False

4.	Stairs in a means of egress system must be at least 44 inches (1 120 m) wide. (273)

A.	True

B.	False

5.	Ladders are allowed in means of egress systems for unlimited purposes. (276)

A.	True

B.	False

6.	Exit illumination requirements are the same for all occupancy classifications. (276)

A.	True

B.	False

7.	Emergency lights may be powered by batteries. (277)

A.	True

B.	False

8.	Floor-level exit signs must be between 8 and 10 inches (200 mm and 250 mm) above the floor surface. (277)

A.	True

B.	False

9.	Occupant load should be established during plans review. (278)

A.	True

B.	False

10.	Which of the following provides the highest degree of fire protection of stair enclosures? (266-267)

A.	Horizontal exit

B.	Exit passageway

C.	Fireproof passageway

D.	Smokeproof enclosure

11.	Which of the following is the MAXIMUM length of a ramp in a means of egress system? (274)

A.	10 feet (3.04 m)

B.	20 feet (6.09 m)

C.	30 feet (9.14 m)

D.	40 feet (12.19 m)

12.	Letters on an exit marking must be at least ___ inches (mm) high. (277)

A.	6 (150)

B.	8 (200)

C.	10 (250)

D.	12	(300)

Directions:	Write a brief answer to the questions below.

13.	Upon what three factors is the fire-resistance rating of a wall based? (272)

14.	What are three common problems with fire escape stairs? (275)

15.	What is the formula for determining occupant load? (279)