Chapter 8 Quiz Answers

1.	B

2.	B

3.	A

4.	B

5.	A

6.	B

7.	A

8.	A

9.	C

10.	B

11.	B

12.	A

13.	Answer should include at least three of the following:

Check for obstructions near hydrant.

Check direction of hydrant outlets.

Check for mechanical damage to the hydrant.

Check the condition of paint for rust or corrosion; ensure ensure discharge outlet caps are not painted shut.

Check water flow by having hydrant fully opened.

Check to ensure a dry-barrel hydrant drains when stem valve is closed.

14. 	Answer should include at least five of the following:

Wear protective equipment.

Erect traffic safety signs on busy streets.

Tighten caps on hydrant outlets not being used.

Do not stand in front of closed caps.

Do not lean over top of a hydrant when operating.

Do not flow water during freezing weather.

15.	 Determine which gpm (L/min) scale should be used.

Locate and plot static pressure on vertical scale at 0 gpm (0 L/min).

Locate total water flow measured during test on chart.

Locate residual pressure noted during test on chart.

Plot residual pressure above total water flow measured.

Draw straight line from static pressure point through residual pressure point on water-flow scale.

Read gpm (L/min) available at 20 psi (140 kPa) and record the figure; this reading represents total available water.

Chapter 8 Test Answers

Objective 1

1.	A

2.	C

3.	B

4.	D

5.	A

Objective 2

6.	D

7.	C

8.	C

9.	A

10.	A

11.	D

Objective 3

12.	B

13.	D

Objective 4

14.	A

15.	A

Objective 5

16.	B

17.	C

18.	D

19.	C

20.	C

Objective 6

21.	A

22.	A

23.	D

24.	B

Objective 7

25.	C

26.	D

Objective 8

27.	B

28.	C

Objective 9

29.	A

30.	D

Objective 10

31.	A

32.	C

Objective 11

This objective is measured in Learning Activity 8-II-1.