Chapter 6 Quiz

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions:	Write the correct answers on the blanks provided.

1.	Tied fire walls are self-supporting and independent of the building frame. (202-203)

A.	True

B.	False

2.	Shaft walls are usually load-bearing. (206)

A.	True

B.	False

3.	The primary function of a roof is to protect the structure from weather. (208)

A.	True

B.	False

4.	Wood floors can be laid directly onto a soil subfloor. (212)

A.	True

B.	False

5.	Access stairs are not required to be a part of the means of egress system. (217)

A.	True

B.	False

6.	Solid-core doors are better fire barriers than panel or hollow-core doors. (226)

A.	True

B.	False

7.	Doors with ratings up to 3 hours can be equipped with glass panels. (233)

A.	True

B.	False

8.	Horizontal sliding windows include a large number of narrow overlapping glass sections that swing outward. (236)

A.	True

B.	False

9.	The number of pipe chases depends upon building size and design. (248)

A.	True

B.	False

10.	Which of the following statements regarding protected stairs is MOST accurate? (220)

A.	They generally serve five or more stories.

B.	They do not affect the safety of occupants.

C.	They are secondary egress paths from floors below grade level.

D.	They are enclosed with fire-rated construction depending on building height.

11.	Which of the following types of fire doors is usually held open by a fusible link and cannot be used to protect openings in walls that are required parts of a means of egress? (230)

A.	Swinging

B.	Rolling steel

C.	Horizontal sliding

D.	Horizontal folding

12.	Which of the following statements regarding injury prevention around hoistway doors is LEAST accurate? (246)

A.	They are equipped with locks.

B.	They are equipped with electrical interlocks.

C.	All doors must be closed or the elevator will not run.

D.	A moving car will stay in motion if a hoistway door is open.

Directions:	Write a brief answer to the questions below.

13.	What are three factors that determine the type, size, and location of doors in a building? (223)

14.	What are the possible hourly fire-protection ratings of fire doors? (228)

15.	What are three components of heating, ventilating, and air-conditioning (HVAC) systems? (251)