Chapter 16 Test

| Name: |  | Date: |  |
| --- | --- | --- | --- |

Directions: Write the correct letter on the blank before each question.

Objective 1:

Discuss the need for a plans review.

1.	Who administers the plans review? (679)

A.	The owner/occupant

B.	The local fire marshal

C.	The building contractor

D.	The local building official

2.	The plans review process should include all of the following EXCEPT representatives of the ___ department. (679)

A.	fire

B.	zoning

C.	building

D.	code enforcement

3.	Which of the following statements regarding plans review is MOST accurate? (680)

A.	Plans reviews must include members of the legal department.

B.	Plans reviews do not begin until after construction has started.

C.	Plans reviews help determine the boundaries between builders and the building department.

D.	Plans reviews are the responsibility of an Inspector II, but an Inspector I should be familiar with the process.

Objective 2:

Describe each of the four main types of plan views.

4.	Working drawings should include a title block with which of the following included? (689)

A.	Name of owner of building

B.	Code official’s stamp or seal

C.	Date the project will be complete

D.	Name of person checking final drawings

5.	Which views are two-dimensional views of a site or building as seen from directly above the area? (690)

A.	Plan views

B.	Detailed views

C.	Elevation views

D.	Sectional views

6.	Which views are two-dimensional views of a building as seen from the exterior? (694)

A.	Plan views

B.	Detailed views

C.	Elevation views

D.	Sectional views

7.	Which views are vertical views of a building as if it were cut into two parts? (696)

A.	Plan views

B.	Detailed views

C.	Elevation views

D.	Sectional views

8.	Which views are provided when it is necessary to show a feature in larger size than what is on the small-scale floor plan or elevation drawings? (697)

A.	Plan views

B.	Detailed views

C.	Elevation views

D.	Sectional views

9.	The ___ plan identifies conditions currently existing on site and relates information needed to locate the building. (690)

A.	site

B.	floor

C.	foundation

D.	construction

10.	Which of the following display the existing grade elevations in feet (meters) and decimal fractions of a foot (meter)? (690)

A.	Floor plans

B.	Grade levels

C.	Contour lines

D.	Lot dimensions

11.	Floor plans include all of the following EXCEPT: (693)

A.	walls.

B.	doors.

C.	sprinklers.

D.	ceiling joists.

12.		Which of the following is symbolized on site plans by parallel lines? (694)

A.	Interior walls

B.	Exterior walls

C.	Windows and doors

D.	Standard hinged door

13.	A rectangular building will have ____ exterior elevation views. (694)

A.	1

B.	2

C.	3

D.	4

14.	Sectional views include all of the following construction details EXCEPT: (696)

A.	the floor.

B.	the foundation.

C.	exterior walls.

D.	doors and windows.

Objective 3:

Describe the types of system plans that require review.

15.	Mechanical systems should be included on ___ plans. (698)

A.	site

B.	floor

C.	mechanical

D.	construction

16.	Inspectors must ensure that mechanical systems include: (698)

A.	HVAC access.

B.	elevator access.

C.	control dampers.

D.	fire alarm control panels.

17.	Which of the following should NOT be checked during inspections of mechanical system plans? (700)

A.	Sizes of fire-resistant walls

B.	Style and design of system

C.	Locations of smoke detectors

D.	Type of refrigerant (for health hazards)

18.	When checking exit illumination, inspectors must evaluate: (701)

A.	size of exit signs.

B.	level of illumination.

C.	exit illumination placement.

D.	correct number of exit signs.

19.	Why should plumbing systems be reviewed? (702)

A.	To determine if storm drains are adequate for the building

B.	To determine if wastewater piping is in proper working order

C.	To determine if systems used to capture contaminated water are in place

D.	To determine if water supply is adequate to support fire-protection systems

20.	When checking sprinkler systems, inspectors must first determine: (703)

A.	occupant load.

B.	storage capacity.

C.	hydraulic calculations.

D.	classification of the hazard.

21.	Sprinkler systems should be checked by inspectors for: (703)

A.	types of piping.

B.	hydrant locations.

C.	number of pipe fittings.

D.	water supply connections.

22.	Sprinklers should be installed in accordance with the ___ listing of the sprinkler. (703)

A.	Underwriters Laboratories (UL)

B.	National Fire Protection Association® (NFPA®)

C.	American National Standards Institute (ANSI)

D.	National Institute for Occupational Safety and Health (NIOSH)

23.	Sprinkler system size is based on the: (703)

A.	total occupant load of the entire building

B.	occupancy type of the area to be covered

C.	total square footage (square meters) of the entire building

D.	total square footage (square meters) of floor area that a single riser and control valve can protect

24.	Special-agent fire-extinguishing systems plans should include: (704)

A.	FDC location.

B.	system classification.

C.	discharge control valve locations.

D.	concentration of extinguishing agent to be developed.

25.	Which of the following is NOT a function of fire detection and alarm systems? (706)

A.	Elevator control

B.	Stair pressurization

C.	Supervision of alarm systems

D.	Doors that lock automatically when alarm activates

Objective 4:

Discuss field verification inspections.

26.	What is the purpose of field verification inspections? (711)

A.	Provide inspectors with a checklist for specific requirements of building’s systems

B.	Aid in ensuring local fire and life safety requirements can be addressed before conflict occurs

C.	Enable plans examiners to discover discrepancies or omissions in building plan before construction begins

D.	Verify that construction activities conform to the approved plans that were submitted for review and permit

27.	What protective clothing should be worn for site visits? (712)

A.	Eye and hearing protection

B.	Class A hazardous materials suits

C.	Full personal protective equipment

D.	Personal protective equipment and self-contained breathing apparatus

28.	Which action should be performed FIRST during a construction site visit? (713)

A.	Schedule a date for the next visit.

B.	Use a checklist to record items as they are inspected.

C.	Check in with the general contractor before entering the site.

D.	Compare construction plans on site to the ones maintained by the building office.

29.	Which of the following is NOT an action to be performed during a construction site visit? (713)

A.	Develop a report noting the items inspected.

B.	Notify the general contractor when violations are found.

C.	Explain the specific items or activities that must be verified.

D.	Ensure that all violations are corrected before leaving the site.